## Slide 1: Initial Project Approach
Android app for the user interface
Use the Laird BL600 module for sensor device processing
Use the MMA8653FC accelerometer for detecting movement
Communication over Bluetooth Low Energy
Implement a prototype on Dr. Jovanov’s development board
Explore over-the-air programming of the BL600

## Slide 2: BLE Profile Implementation
Defined a custom BLE service
  Arm state characteristic
    Read/write
    0 – disarmed
    1 – armed
  Alarm characteristic
    Notify only
    0 – No alarm
    1 – Alarm

## Slide 3: Unexpected Issues
Getting Over-The-Air programming to work was slower than expected
  Needed a BL620 dongle for OTA to work (this was not immediately obvious)
  Development kit pin configuration example confusion
Unable to get the MMA8653FC accelerometer on Dr. Jovanov’s development board to work
  Verified the I2C signals coming from the BL600 were correct
  Verified the BL600 could communicate over I2C to the capacitance-to-digital converter
  Tried 3 different development boards

## Slide 4: Modified Project Approach
Use the capacitance-to-digital converter with a touch sensor attached to a water bottle
Grasping the water bottle will be treated as the alarm condition

## Slide 5: Project Test Plan
Verify the app can pair with the device when the device is powered
Verify the device is shown to be initially disarmed in app
Verify the device does not trigger an alarm when in disarm state
Verify the device can be armed from app
Verify the device triggers an alarm when in armed state
Verify the alarm is triggered when the water bottle is grasped with the whole hand
Verify the app alerts the user when the alarm is triggered
Verify the app can disarm the device when it is in the alarm state

## Slide 6: Demo