## Slide 1: Attachable Motion-Detector Security System (AMDeSS)
Final Presentation
Caleb Stewart & John Wilkes

## Slide 2: Problem
Personal belongings left unattended in a public place are an easy target for thieves
www.airsafe.com

## Slide 3: Solution
AMDeSS is an attachable motion device that alerts a user via smartphone when it is moved
www.fotosearch.com www.businesswire.com www.telegraph.co.uk www.clipartpanda.com

## Slide 4: Existing Products

## Slide 5: Market Research - LiveWatch
Customizable
Outside doors
Inside motion sensors
Smartphone alerts
https://www.livewatch.com

## Slide 6: Market Research - SimpliSafe
Customizable and easy to install
Supports multiple types of sensors (e.g. motion sensor, smoke detector, CO sensor, etc.)
System supports up to 41 sensors
Sends text alerts
http://simplisafe.com

## Slide 7: AMDeSS vs. Existing Products
AMDeSS leverages Bluetooth to allow easy mobile deployment
AMDeSS can be used to complement a more complete in-home security system
en.wikipedia.org

## Slide 8: AMDeSS Implementation

## Slide 9: Initial Project Approach
Android app for the user interface
Use the Laird BL600 module for sensor device processing
Use the MMA8653FC accelerometer for detecting movement
Communication over Bluetooth Low Energy
Implement a prototype on Dr. Jovanov’s development board
Explore over-the-air programming of the BL600

## Slide 10: BLE Profile Implementation
Defined a custom BLE service
  Arm state characteristic
    Read/write
    0 – disarmed
    1 – armed
  Alarm characteristic
    Notify only
    0 – No alarm
    1 – Alarm

## Slide 11: Unexpected Issues
Getting Over-The-Air programming to work was slower than expected
  Needed a BL620 dongle for OTA to work (this was not immediately obvious)
  Development kit pin configuration example confusion
Unable to get the MMA8653FC accelerometer on Dr. Jovanov’s development board to work
  Verified the I2C signals coming from the BL600 were correct
  Verified the BL600 could communicate over I2C to the capacitance-to-digital converter
  Tried 3 different development boards

## Slide 12: Modified Project Approach
Use the capacitance-to-digital converter with a touch sensor attached to a water bottle
Grasping the water bottle will be treated as the alarm condition

## Slide 13: Project Test Plan
Verify the app can pair with the device when the device is powered
Verify the device is shown to be initially disarmed in app
Verify the device does not trigger an alarm when in disarm state
Verify the device can be armed from app
Verify the device triggers an alarm when in armed state
Verify the alarm is triggered when the water bottle is grasped with the whole hand
Verify the app alerts the user when the alarm is triggered
Verify the app can disarm the device when it is in the alarm state

## Slide 14: Demo

## Slide 15: Questions?