## Slide 1: Midterm Progress Report
Attachable Motion-Detector Security System (AMDeSS)

## Slide 2: Outline
The AMDeSS Concept
What we’ve accomplished so far
What we’re working on now
Goals for the remainder of the semester

## Slide 3: The AMDeSS Concept

## Slide 4: AMDeSS Concept Summary
AMDeSS is a physically attachable, motion-detecting security module that the user can interact with via a smartphone application.

## Slide 5: AMDeSS Use Case
User configures AMDeSS device via smartphone app
User attaches AMDeSS device in desired location (on door, window, etc.)
User arms the AMDeSS device from smartphone app
When AMDeSS device is physically displaced, an alert is sent to the smartphone app and the user is notified
User acknowledges the alert/disarms the AMDeSS device
User takes appropriate action at his discretion
  Ignore alert and re-arm device
  Command AMDeSS device to panic
  Silence AMDeSS device (if already in panic mode)

## Slide 6: What we’ve done so far

## Slide 7: Accomplishments
Started with Dr. Jovanov’s development board
  Attempted Bluetooth connection – device recognized on Laird app
  Considered trying to program over UART through Teensy board (bad idea)
  Realized we did not have a way to determine whether or not OTA programming attempts were successful.
  Decided we needed to start with the Laird development board and then move to OTA programming later
Obtained the Laird development board for the BL600 module
Started learning the Android environment for the smartphone app
Started learning the smartBASIC language and APIs for the BL600
Developed state diagrams for the sensor device and the smartphone
Learned the basics of BLE communication
  General protocol overview
  Android BLE API
  smartBASIC BLE API
  Pairing vs. bonding
Successfully advertised over BLE from BL600 to smartphone
Successfully paired BL600 with smartphone

## Slide 8: Smartphone State Diagram

## Slide 9: Sensor Device State Diagram
Already paired with a master?
Sleep
Ready
Pairing
Armed
Alarm!
Do Command
Y
N
Button press
Timeout
Paired/connected with smartphone
Command received
Command completed
Arm command received
Disarm command received
Disarm command received
Accelerometer interrupt

## Slide 10: What we’re working on now

## Slide 11: Tasks In Progress/Next Steps
Get BL600 and smartphone communicating via BLE profiles/services
Define the set of BLE services that will be used when operating over BLE
Implement app user interface
Interface with accelerometer from BL600

## Slide 12: Where we’re going

## Slide 13: Goals for remainder of semester
User can pair/bond with BL600 via smartphone (10/24)
User can arm/disarm device (10/24)
Get OTA programming working on Dr. Jovanov’s development board (11/1)
User is notified when the BL600 detects motion (11/7)
User can name device
User can add multiple devices
Wifi mode

## Slide 14: Outstanding Issues/Questions
What are the requirements/expectations for the paper?
Which goals are critical and which are stretch goals?

## Slide 15: Questions?