## Slide 1: Midterm Progress Report
Attachable Motion-Detector Security System (AMDeSS)

## Slide 2: Outline
The AMDeSS Concept
What we’ve accomplished so far
What we’re working on now
Where we’re going

## Slide 3: The AMDeSS Concept

## Slide 4: AMDeSS Concept Summary
AMDeSS is a physically attachable, motion-detecting security module that the user can interact with via a smartphone application.

## Slide 5: AMDeSS Use Case
User configures the device via smartphone app
User attaches the device in desired location (on door, window, etc.)
User arms the device from smartphone app
When the device is physically displaced, an alert is sent to the smartphone app and the user is notified
User acknowledges the alert/disarms the device
User takes appropriate action at his discretion
  Ignore alert and re-arm device
  Command the device to panic
  Silence the device (if already in panic mode)

## Slide 6: What we’ve done so far

## Slide 7: Accomplishments
Started with Dr. Jovanov’s development board
  Attempted Bluetooth connection – device recognized on Laird app
  Considered trying to program over UART through Teensy board
  Realized we did not have a way to determine whether or not over-the-air (OTA) programming attempts were successful.
  Decided we needed to start with the Laird development kit and then move to OTA programming later
Obtained the Laird development board for the BL600 module
Started learning the Android environment for the smartphone app
Started learning the smartBASIC language and APIs for the BL600
Developed state diagrams for the sensor device and the smartphone
Learned the basics of BLE communication
Successfully advertised over BLE from BL600 to smartphone
Successfully paired BL600 with smartphone

## Slide 8: Smartphone State Diagram
Ready
Attempt to Pair
Alarm
Is device still in alarm state?
Connected?
Is device in alarm state?
Startup
Get device info
Connect to a device
Send commands
Send commands
Y
Y
Y
N
N
N
Add device
Miss keep alive or receive alarm message – add to alarming devices list
Disarm device
Miss keep alive or receive alarm message – add to alarming devices list
Paired – add device to list
Timeout
Attempt to connect to all known devices

## Slide 9: Sensor Device State Diagram
Already paired with a master?
Sleep
Ready
Pairing
Armed
Alarm!
Do Command
Y
N
Button press
Timeout
Paired/connected with smartphone
Command received
Command completed
Arm command received
Disarm command received
Disarm command received
Accelerometer interrupt

## Slide 10: What we’re working on now

## Slide 11: Tasks In Progress/Next Steps
Get BL600 and smartphone communicating via BLE profiles/services
Define the set of services that will be used when operating over BLE
Try to get the BL600 module on Dr. Jovanov’s development board set up so that it can be reprogrammed OTA as we progress
Implement app user interface
Interface with accelerometer from BL600

## Slide 12: Where we’re going

## Slide 13: Goals for remainder of semester
User can pair with device via smartphone (app/device)
User can arm/disarm device (app/device)
Get OTA programming working on Dr. Jovanov’s development board (device)
User is notified when the armed device detects motion (app/device)
User can name device (app/device)
User can view device diagnostics (app/device)
Write project paper

## Slide 14: Stretch Goals
User can add multiple devices
Enable encrypted communication
Enable Wifi mode as an alternate to BLE
Add LED/buzzer to device platform

## Slide 15: Questions?